## Slide 1: Manual of DAB3 Model with Multiple Modulations
Huixue Liu
Zhiqing Yang
With three operating modes: SPS, ADCC and IADCC

## Slide 2: How to Run the Model
Step 1: Run the file: Def_System.m
  Get primary side duty cycle d1
  Get secondary side duty cycle d2
  Get phase shifting dp
Step 2: Run the model in PLECS: DAB3_MBCC.slx
  All modules can directly call the objects of the file.
    i.e.: call DAB3 object

## Slide 3: How to Set Operating Point
Step 1: Open the main file: Def_System.m
All the variables in the circuit will be defined here using Object-Oriented Methods. Here you can:
  Set the simulation duration with simtime ;
  Set the fixed-voltage value side with fix_flag ;
    i.e.: fix_flag = 'input side‘; that means the input voltage has a fixed value, and the output voltage will be influenced by the other parameters.

## Slide 4: How to Set Operating Point
Step 2: Open the file: Def_SetOP.m
  Set power value
    Set the power rating with OP.Pn;
    Set the power flow in per-unit system with OP.P_op ;
  Set voltage value
    Set the fixed-voltage side value with OP.V_fix ;
    Set the voltage ratio in per-unit system with OP.r_op ;
    The operating input and output voltage will be calculated according to the above settings.

## Slide 5: How to Set Other Objects
Step 3: Open the file: Def_DAB3.m
  Set the Three-Phase-DAB parameters as required;
  Initial voltage of capacitors depends on the OP.Vn_in and OP.Vn_out in Def_SetOP.m file.
Step 4: Open the file: Def_Mod.m
  Set the dead time parameters in modulator object;
  Decide whether to use ICC mode with Mod.ICC_flag .
  Choose the different dead time mode with Mod.td_mode .

## Slide 6: How to Set Other Objects
Step 5: Open the file: Def_Ctrl.m
  Set the switching frequency with Ctrl.f_sw and sampling frequency with Ctrl.f_sp in controller object;
  Decide whether to use dead time compensation with Ctrl.td_flag.
  Choose the different operating mode with Ctrl.OP_flag
Tips: parameters can be change easily in the main define file

## Slide 7: How to Set Other Objects
Step 6: File Def_Plot.m
  Show the operating point and the operating range of the circuit;
  Without modification.